## Slide 1
Siemens S7-200 PLC Programming
Module 16 — Interrupt Instructions
Day 26 | Advanced Level | Duration: 2 Hours
Siemens S7-200 PLC Programming | STEP 7-Micro/WIN
© S7-200 PLC Course

## Slide 2
Day 26 — Agenda
Module 16 | Day 26
1
Interrupt কী? কখন ব্যবহার করবেন?
2
Interrupt Types — I/O, Timer, Communication
3
ATCH — Attach Interrupt Routine
4
DTCH — Detach Interrupt Routine
5
ENI / DISI — Enable / Disable Interrupt
6
CRETI — Conditional Return from Interrupt
7
Interrupt Event Table (Event 0~33)
8
Practical: Emergency Stop with Interrupt
Siemens S7-200 PLC Programming | STEP 7-Micro/WIN
Module 16 | Day 26

## Slide 3
Interrupt — কীভাবে কাজ করে
Module 16 | Day 26
Interrupt মানে:
Program চলার মাঝে হঠাৎ একটি জরুরি ঘটনা ঘটলে
Main Program থামিয়ে Interrupt Routine (INT) চালু হয়
INT শেষে আবার Main Program চলতে থাকে
কেন Scan Cycle এর চেয়ে ভালো?
Scan Time: 1~10ms — এটুকু দেরি অনেক সময় অনেক বেশি
Emergency Stop: মাইক্রোসেকেন্ডে Response দরকার
HSC, PLS, Timer Events এ Precise Timing দরকার
Interrupt Priority (উচ্চ থেকে নিম্ন):
1st: Communication Interrupts
2nd: I/O Interrupt (Rising/Falling Edge)
3rd: Time-based Interrupts
Important Rules:
INT Routine সংক্ষিপ্ত রাখুন
INT এ CALL, FOR, END, STOP ব্যবহার করা যাবে না
💡 Interrupt Routine যত ছোট তত ভালো — মূল কাজটুকুই শুধু করুন!
Siemens S7-200 PLC Programming | STEP 7-Micro/WIN
Module 16 | Day 26

## Slide 4
Interrupt Event Table — গুরুত্বপূর্ণ Events
Module 16 | Day 26
Event #
Event Type
Trigger
সাধারণ ব্যবহার
0
I0.0 Rising Edge
I0.0: 0→1
Emergency Button Press
1
I0.0 Falling Edge
I0.0: 1→0
Button Release detect
2
I0.1 Rising Edge
I0.1: 0→1
Encoder Z-pulse
8
Port 0 Receive
Serial Data Received
Barcode / HMI data
9
Port 0 Transmit
Tx Buffer Empty
Next byte send
10
Timed Interrupt 0
Every N ms
PID, Regular sampling
11
Timed Interrupt 1
Every N ms
Second PID loop
12
HSC0 CV=PV
HSC0 Count Match
Position target reached
19
PLS0 Complete
Pulse train done
Stepper motion complete
Siemens S7-200 PLC Programming | STEP 7-Micro/WIN
Module 16 | Day 26

## Slide 5
ATCH, DTCH, ENI, DISI — Interrupt Control
Module 16 | Day 26
ATCH (Attach Interrupt):
একটি Event কে একটি INT Routine এর সাথে যুক্ত করে
ATCH INT_0, 0 → Event 0 (I0.0 Rising) → INT_0 চালাবে
DTCH (Detach Interrupt):
Event থেকে INT Routine বিচ্ছিন্ন করে
DTCH 0 → Event 0 এর Interrupt বন্ধ করে
ENI (Enable All Interrupts):
সব Interrupt চালু করে
Program শুরুতে একবার ENI দিতে হয়
DISI (Disable All Interrupts):
সব Interrupt সাময়িক বন্ধ করে
Critical Section এর সময় ব্যবহার
Setup Sequence:
Step 1: ATCH INT_0, Event#
Step 2: ENI (Enable করুন)
INT_0 Block এ Response Code লিখুন
💡 ENI ছাড়া ATCH করলেও Interrupt কাজ করবে না — ENI অবশ্যই দিতে হবে!
Siemens S7-200 PLC Programming | STEP 7-Micro/WIN
Module 16 | Day 26

## Slide 6
⚙ PRACTICAL
Practical: Emergency Stop with Interrupt
Module 16 | Day 26
🎯 Objective: Emergency Button চাপলে সাথে সাথে সব Output বন্ধ হবে
1
I0.0 = Emergency Stop Button (N.C. — সবসময় Closed)
2
I0.0 Falling Edge (0→1, Button Press) = Event 1
3
Main Program: ATCH INT_0, 1 (Event 1 Attach)
4
Main Program: ENI (Interrupt Enable করুন)
5
INT_0 Block এ: MOV_B +0, QB0 (All Output OFF)
6
INT_0 Block এ: MOV_B +0, QB1 (All Output OFF)
7
INT_0 Block এ: STOP (CPU Stop করুন)
8
Test: Normal operation চলার সময় E-Stop চাপুন
Siemens S7-200 PLC Programming | STEP 7-Micro/WIN
Module 16 | Day 26

## Slide 7
📋 Session Summary
Module 16 — Day 26: Interrupt Instructions
✅ Key Takeaways
▸ Interrupt: Scan wait না করে সাথে সাথে Response
▸ ATCH: Event + INT Routine যুক্ত করে
▸ ENI: সব Interrupt চালু করে
▸ DISI: সব Interrupt সাময়িক বন্ধ করে
▸ INT Routine ছোট রাখুন — শুধু জরুরি কাজ
⏭ Next Session
Day 27 (Module 17): • Communications শুরু • PPI Protocol • NETR ও NETW Instructions
Siemens S7-200 PLC Programming | STEP 7-Micro/WIN
Module 16 | Day 26

## Slide 8
Siemens S7-200 PLC Programming
Module 17 — Communications
Day 27 | Advanced Level | Duration: 2 Hours
Siemens S7-200 PLC Programming | STEP 7-Micro/WIN
© S7-200 PLC Course

## Slide 9
Day 27 — Agenda
Module 17 | Day 27
1
S7-200 Communication Ports (Port 0, Port 1)
2
PPI Protocol — Network Read/Write
3
NETR ও NETW Instructions
4
Freeport Mode — Custom Serial Protocol
5
XMT (Transmit) ও RCV (Receive)
6
USS Protocol — Variable Speed Drive
7
Modbus RTU Protocol
8
HMI (TD400C) সংযোগ
Siemens S7-200 PLC Programming | STEP 7-Micro/WIN
Module 17 | Day 27

## Slide 10
S7-200 Communication Overview
Module 17 | Day 27
Physical Interface:
RS-485 Serial Port (Port 0 ও Port 1)
9-pin D-sub Connector
Half-duplex, 2-wire
Communication Protocols:
PPI (Point-to-Point Interface) — Siemens proprietary
MPI (Multi-Point Interface) — Multi-device
Freeport — Custom ASCII/Binary protocol
USS — Variable Speed Drive Control
Modbus RTU — Industry Standard
Baud Rates:
PPI: 9600 বা 19200 bps
Freeport: 1200 ~ 115200 bps
PPI Network:
সর্বোচ্চ 126টি Device একটি Network এ
Master-Slave Architecture
💡 S7-200 একই সময়ে Port 0 এ STEP 7-Micro/WIN এবং Port 1 এ HMI connect করা যায়!
Siemens S7-200 PLC Programming | STEP 7-Micro/WIN
Module 17 | Day 27

## Slide 11
Communication Instructions
Module 17 | Day 27
Instruction
Protocol
কাজ
ব্যবহার
NETR
PPI
Network Read — অন্য PLC থেকে Data পড়া
Multi-PLC system
NETW
PPI
Network Write — অন্য PLC তে Data লেখা
PLC → PLC data share
XMT
Freeport
Serial Data পাঠানো
Printer, Barcode, HMI
RCV
Freeport
Serial Data গ্রহণ করা
Barcode reader, PC
USS_INIT
USS
USS Drive Initialize
VFD setup
USS_CTRL
USS
Drive Speed Control
Motor speed command
USS_RPM_R
USS
Drive Parameter Read
Drive status read
MBUS_INIT
Modbus
Modbus Slave Initialize
HMI, SCADA connect
MBUS_SLAVE
Modbus
Modbus Slave Execution
Regular call in main
Siemens S7-200 PLC Programming | STEP 7-Micro/WIN
Module 17 | Day 27

## Slide 12
Freeport — XMT/RCV ব্যবহার
Module 17 | Day 27
Freeport Setup:
SMB30 এ Baud Rate ও Mode Configure করুন
SMB30 = 16#09 → 9600 bps, 8N1, Freeport Mode
XMT (Transmit):
XMT VB100, 0 → Port 0 দিয়ে VB100 এর Buffer পাঠায়
VB100 = Message Length, VB101~ = Data
Transmit Done → Event 9 Interrupt Fire করে
RCV (Receive):
SMB86~SMB94 এ Receive Conditions Configure করুন
RCV VB200, 0 → Port 0 থেকে VB200 তে Data গ্রহণ
Receive Done → Event 8 Interrupt
Example: Barcode Scanner
Barcode Scanner → RS-232 → USB/RS-485 Converter → Port 0
RCV দিয়ে Barcode String গ্রহণ করুন
SFND দিয়ে Product Code Match করুন
💡 Freeport দিয়ে যেকোনো RS-232/RS-485 Device এর সাথে S7-200 কে যুক্ত করা যায়!
Siemens S7-200 PLC Programming | STEP 7-Micro/WIN
Module 17 | Day 27

## Slide 13
📋 Session Summary
Module 17 — Day 27: Communications
✅ Key Takeaways
▸ PPI: Siemens PLC to PLC — NETR/NETW
▸ Freeport: Custom Serial — XMT/RCV
▸ USS: VFD/Drive Control
▸ Modbus RTU: Industry standard — HMI/SCADA
▸ Port 0 = PC/Programming, Port 1 = HMI/Device
⏭ Next Session
Day 28 (Module 18): • Subroutines ও Structured Programming • Final Projects শুরু • Traffic Light System
Siemens S7-200 PLC Programming | STEP 7-Micro/WIN
Module 17 | Day 27

## Slide 14
Siemens S7-200 PLC Programming
Module 18 — Subroutines & Structured Programming
Day 28 | Advanced Level | Duration: 2 Hours
Siemens S7-200 PLC Programming | STEP 7-Micro/WIN
© S7-200 PLC Course

## Slide 15
Day 28 — Agenda
Module 18 | Day 28
1
Subroutine (SBR) কী এবং কেন দরকার?
2
Local Variable ও Parameter Passing
3
Structured Programming Approach
4
Cross Reference ব্যবহার
5
Status Chart দিয়ে Debug করা
6
Project 1: Traffic Light Control System
Siemens S7-200 PLC Programming | STEP 7-Micro/WIN
Module 18 | Day 28

## Slide 16
Subroutine — Modular Programming
Module 18 | Day 28
কেন Subroutine?
একই Code বারবার লেখার দরকার নেই
Program কে ছোট ছোট ব্লকে ভাগ করা যায়
Testing সহজ হয়
Code Reuse — Library তৈরি করা যায়
S7-200 তে Subroutine:
SBR_0, SBR_1 ... SBR_63 (64টি পর্যন্ত)
CALL SBR_0 দিয়ে Call করা হয়
RET বা CRET দিয়ে Return হয়
Local Variable:
IN: Input Parameter (Caller থেকে দেওয়া)
OUT: Output Parameter (SBR থেকে ফেরত)
IN_OUT: উভয় দিকে
TEMP: Subroutine এর ভেতরে সাময়িক
Calling with Parameters:
CALL SBR_0, VW100, VW200 (IN=VW100, OUT=VW200)
💡 Parameter ব্যবহার করে Subroutine আরও Flexible ও Reusable হয়!
Siemens S7-200 PLC Programming | STEP 7-Micro/WIN
Module 18 | Day 28

## Slide 17
⚙ PRACTICAL
Project 1: Traffic Light Control System
Module 18 | Day 28
🎯 Objective: ৩টি Signal এর Traffic Light — Green 30s, Yellow 5s, Red 30s
1
Q0.0=Red, Q0.1=Yellow, Q0.2=Green (Road A)
2
Q0.3=Red, Q0.4=Yellow, Q0.5=Green (Road B)
3
MB10 = Traffic Step (0=Init, 1=A-Green, 2=A-Yellow, 3=B-Green, 4=B-Yellow)
4
SBR_0: Traffic_Timer Subroutine (IN: PT, OUT: Done Bit)
5
Step 1 (MB10==1): A-Green ON, B-Red ON → Timer 30s
6
Step 2 (MB10==2): A-Yellow ON → Timer 5s
7
Step 3 (MB10==3): B-Green ON, A-Red ON → Timer 30s
8
Step 4 (MB10==4): B-Yellow ON → Timer 5s → Back to Step 1
Siemens S7-200 PLC Programming | STEP 7-Micro/WIN
Module 18 | Day 28

## Slide 18
📋 Session Summary
Module 18 — Day 28: Subroutines
✅ Key Takeaways
▸ SBR: Reusable code block
▸ CALL দিয়ে যেকোনো জায়গা থেকে চালানো যায়
▸ Local Variable দিয়ে Parameter pass করা যায়
▸ Cross Reference: কোন Variable কোথায় আছে
▸ Traffic Light: Step Sequencer + Timer এর সমন্বয়
⏭ Next Session
Day 29: • Final Projects 2, 3, 4 • Conveyor Sorting System • Water Level Control • PID Temperature Control
Siemens S7-200 PLC Programming | STEP 7-Micro/WIN
Module 18 | Day 28

## Slide 19
Siemens S7-200 PLC Programming
Module 18 — Real-World Projects
Day 29 | Final Projects Day | Duration: 3 Hours
Siemens S7-200 PLC Programming | STEP 7-Micro/WIN
© S7-200 PLC Course

## Slide 20
Day 29 — Projects Agenda
Module 18 | Day 29
1
Project 2: Conveyor Belt with Product Sorting
2
Project 3: Water Level Control System
3
Project 4: PID Temperature Controller
4
Project 5: Batch Process with Recipe
5
Debugging ও Troubleshooting Techniques
6
Program Documentation Best Practices
Siemens S7-200 PLC Programming | STEP 7-Micro/WIN
Module 18 | Day 29

## Slide 21
⚙ PRACTICAL
Project 2: Conveyor Belt with Sorting
Module 18 | Day 29
🎯 Objective: Product Size অনুযায়ী ৩টি Bin এ Sort করা
1
I0.0=Start, I0.1=Stop, I0.2=Size Sensor (Analog)
2
Q0.0=Conveyor Motor, Q0.1=Diverter 1, Q0.2=Diverter 2
3
AIW0 = Product Size (0=Small, 1000=Medium, 2000=Large)
4
Network 1: I0.0/I0.1 → Start-Stop Motor (Q0.0)
5
Network 2: <I AIW0,+1000 → Q0.1 (Bin 1 — Small)
6
Network 3: >=I AIW0,+1000 AND <I AIW0,+2000 → Q0.2 (Bin 2)
7
Network 4: >=I AIW0,+2000 → Q0.1+Q0.2 (Bin 3 — Large)
8
SHRB I0.3, M0.0, 8 (Conveyor position tracking)
Siemens S7-200 PLC Programming | STEP 7-Micro/WIN
Module 18 | Day 29

## Slide 22
⚙ PRACTICAL
Project 3: Water Level Control System
Module 18 | Day 29
🎯 Objective: Tank এর Water Level Low/High অনুযায়ী Pump নিয়ন্ত্রণ
1
AIW0 = Level Sensor (0=Empty, 32000=Full)
2
I0.0=High Level Float Switch, I0.1=Low Level Float Switch
3
Q0.0=Inlet Pump, Q0.1=Outlet Valve, Q0.2=Alarm
4
Network 1: <=I AIW0,+6400 → S Q0.0 (Level <20%, Pump ON)
5
Network 2: >=I AIW0,+28800 → R Q0.0 (Level >90%, Pump OFF)
6
Network 3: >=I AIW0,+30000 → Q0.2 (Overflow Alarm)
7
Network 4: I0.0 N.C. → S Q0.1 (Float: Not High → Outlet open)
8
Hysteresis দিয়ে Pump Chattering এড়ানো
Siemens S7-200 PLC Programming | STEP 7-Micro/WIN
Module 18 | Day 29

## Slide 23
⚙ PRACTICAL
Project 4: PID Temperature Controller
Module 18 | Day 29
🎯 Objective: Oven Temperature 180°C তে PID দিয়ে সঠিকভাবে Control করা
1
AIW0 = Thermocouple Input (0~32000 = 0°C~300°C)
2
AQW0 = Heater SSR Output (0~32000 = 0~100% Power)
3
Timed Interrupt (Event 10): Every 100ms → PID Call
4
INT_0: AIW0 কে 0.0~1.0 তে Scale → VD0 (PV)
5
INT_0: VD4 = 0.60 (SP = 180/300 = 0.60)
6
INT_0: PID 0, VD0 (KC=2.5, TI=3.0, TD=0.05)
7
INT_0: VD8 × 32000.0 → AQW0 (Output Scale)
8
Tuning: Monitor PV Response → Adjust KC, TI
Siemens S7-200 PLC Programming | STEP 7-Micro/WIN
Module 18 | Day 29

## Slide 24
📋 Session Summary
Module 18 — Day 29: Real-World Projects
✅ Key Takeaways
▸ Conveyor Sorting: Compare + SHRB + Output
▸ Water Level: Compare + Set/Reset + Hysteresis
▸ PID Controller: Interrupt + Analog + PID
▸ Debugging: Status Chart সবচেয়ে গুরুত্বপূর্ণ Tool
▸ Symbol Table ব্যবহার করলে Code পড়া সহজ হয়
⏭ Next Session
Day 30 (Final Day): • Project 5, 6 — Final Assembly Line • Course Summary • Certification Assessment
Siemens S7-200 PLC Programming | STEP 7-Micro/WIN
Module 18 | Day 29

## Slide 25
Siemens S7-200 PLC Programming
Day 30 — Course Completion & Assessment
Final Day | All Modules Completed | Duration: 3 Hours
Siemens S7-200 PLC Programming | STEP 7-Micro/WIN
© S7-200 PLC Course

## Slide 26
Day 30 — Final Agenda
Day 30 | Final
1
Project 5: Batch Process with Recipe System
2
Project 6: Multi-Station Assembly Line (Capstone)
3
Full Course Summary — 18 Modules Review
4
Career Path ও Industry Certification
5
Final Assessment / Quiz
6
Congratulations & Certificate!
Siemens S7-200 PLC Programming | STEP 7-Micro/WIN
Day 30 | Final

## Slide 27
⚙ PRACTICAL
Project 5: Batch Process with Recipe System
Day 30 | Final
🎯 Objective: 3টি Recipe থেকে নির্বাচন করে Batch Process চালানো
1
VB100~VB109 = Recipe 1 (Speed, Temp, Time, Qty...)
2
VB110~VB119 = Recipe 2
3
VB120~VB129 = Recipe 3
4
IB0 = Recipe Selector Switch
5
BLKMOV দিয়ে Active Recipe লোড করুন
6
Math Instruction দিয়ে Analog Output Scale করুন
7
Step Sequencer দিয়ে Process চালান
8
Counter দিয়ে Batch Quantity গণুন
Siemens S7-200 PLC Programming | STEP 7-Micro/WIN
Day 30 | Final

## Slide 28
Complete Course Summary — 18 Modules
Day 30 | Final
Module
Topic
Key Instructions
Day
01
PLC Basics
Hardware, Scan Cycle, Memory
1-2
02
STEP 7 Software
LAD Editor, Download, Monitor
3
03
Bit Logic
Contacts, Coils, SR, RS
4-6
04
Timers
TON, TONR, TOF
7
05
Counters
CTU, CTD, CTUD, HSC, PLS
8-9
06
Compare
==I, >I, <I, ==R
11
07
Move
MOV, BLKMOV, SWAP
12
08
Integer Math
ADD, SUB, MUL, DIV, INC, DEC
14
09
Float Math + PID
ADD_R, SQRT, SIN, PID
15-16
10
Convert
BCD, ROUND, SEG, ITA
18-19
11
Logical Ops
AND, OR, XOR, INV
20
12
Shift/Rotate
SHL, SHR, ROL, ROR, SHRB
21
13
String
SCPY, SCAT, SFND
22
14
Table
ATT, FIFO, LIFO, FND
23
15
Program Control
JMP, FOR, CALL, WDR
24
16
Interrupt
ATCH, ENI, DISI, CRETI
26
17
Communications
NETR, NETW, XMT, RCV
27
18
Projects
All Instructions Combined
28-30
Siemens S7-200 PLC Programming | STEP 7-Micro/WIN
Day 30 | Final

## Slide 29
🎓 Congratulations!
আপনি Siemens S7-200 PLC Programming Course সম্পন্ন করেছেন!
18 Modules | 30 Days | 60+ Hours of Learning
✅ You can now:
▸ Design ও Program করতে পারবেন যেকোনো Industrial Automation System
▸ Bit Logic, Timer, Counter, Math, PID — সব ব্যবহার করতে পারবেন
▸ HMI, VFD, Modbus Device এর সাথে Communication করতে পারবেন
Siemens S7-200 PLC Programming | STEP 7-Micro/WIN | 30 Days Complete